Technical specification of the subject of performance of the public contract

| Name of contract: | "Purchase of technology for cold stabilization of beverages" |
| --- | --- |

| Client |
| --- |
| Name: | Jiří Sláma |
| Address: | Chlístov 11, 580 01 Okrouhlice |
| IČ: | 72000112 |
| DIČ: | CZ8301032982 |
| Person authorized to act on behalf of the contracting authority: | Jiří Sláma |
| Contact person: | Jiří Sláma |
| Telephone - mobile: | +420 777 242 826 |
| E-mail: | info@vcelarstvi-slama.cz |

Technical parameters of the public contract:

- Technology for cold stabilization of beverages - 1 pc

- possibility of connection to the filling line between the storage tank and the filling line

- power min. 600 l / h

- filling temperature 5 - 20 °C

- connection to stainless steel pipes

- handling in Czech language

- touch screen with a choice of different types of drinks and dosing

- dimensions max. length 2300 mm, width max. 1200 mm, height max. 2000 mm

- dosing into the fluid depending on the flow rate

- digital flow meter with display

- power consumption max. 2 kW

- 230 V electrical connection

The contracting authority does not allow partial performance of the public contract. The tenderer must submit a price offer for a comprehensive set of all machines listed in the Technical Specification of the Subject of Performance of the Public Contract.